IEC-822

4U Industrial

Rackmount Chassis

Optional Redundant hot swappable -48VDC 300 watts p/s available

Note all specifications are subject to change without notice

General Specifications

Dimensions

483 x 177 x 450 WxHxD mm

Weight

Netto 12.8 kg (27.5 lb)

(without backplane, drives and power supply )

Color

Beige

Construction

Heavy-duty steel chassis

Slots

up to 14 boards

Disk drive bay

Three 5ºî drives (accesible from front panel)

and three 3½î drives (one accesible from front)

shock resistant protect against vibration/shock

Cooling fans

85 CFM fan (flow-in) with

air filter on front, 120 x 120 x 25 mm

Controls on Front Panel

Power On/Off switch, RESET button

Keyboard Lock switch

Indicators on Front panel

Power on, HDD activity

Keyboard connector

Pre-wired 5-pin DIN connector on front panel

Speaker

One 8-ohm speaker mounted on fan housing

Environmental

Operating Temperature

0~45°C (0~75°C non-operating)

Altitude

3000 m (10,000 ft.)

Shock

2.5G @ 15-20ms

(35G @ 15-20ms non-operating)

Vibration

5 ~ 17 Hz, 0.1" double amplitude displacement;

17 ~ 500 Hz, 1.5 G acceleration

(operating and non-operating)

Power Supply Options

IPS-ZKS-250A

250 W Power Supply (PS/2 size)

VINTPUT : 95~130 VAC or 180~260 VAC

@ 47~63 Hz,switchable

VOUTPUT (max. load) : +5 V @ 25 A,

+12 V @ 10 A, -5 V @ 0.5 A, -12V @ 0.5 A

VOUTPUT (min. load) : +5V @ 1 A, +12 V @ 0.4 A

IPS-ZKS-250WX

250 W ATX Power Supply (PS/2 size)

VINTPUT : 100~130 VAC or 180~260 VAC

@ 50~60 Hz, switchable

VOUTPUT (max. load) : +3.3 V @ 14 A,

+ 5 V @ 25 A, +12 V @ 12 A, -5 V @ 0.5 A,

-12V @ 1 A, +5 Vsb @ 1.5 A

VOUTPUT (min. load) : +5V @ 3 A, +12 V @ 2 A

IPS-ZKS-300WX

300 W ATX Power Supply (PS/2 size)

VINTPUT : 100~130 VAC or 180~260 VAC

@ 50~60 Hz, switchable

VOUTPUT (max. load) : +3.3 V @ 20 A,

+ 5 V @ 30 A, +12 V @ 12 A, -5 V @ 0.5 A,

-12V @ 1 A, +5 Vsb @ 1.5 A

VOUTPUT (min. load) : +5V @ 3 A, +12 V @ 2 A

Optional Redundant PS/2 size

power supplies

available

Passive Backplane Options

PBI-14S

14-slot ISA Passive Backplane

PBPX-14S7

14-slot PICMG Passive Backplane, 8 ISA, 2

PICMG, 4 PCI with 20-pin ATX, standard AT

and power terminal block

PBPI-14SA

14-slot PICMG Passive Backplane with PCI

bridge, 5 ISA, 2 PICMG, 7 PCI, with 20-pin

ATX, standard AT and power terminal block

PBPI-14S2

Mirrored 14-slot PICMG Passive Backplane

8 ISA, 2 PICMG, 4 PCI in reversed order

Baby-AT or Full-size ATX motherboard

Select any type available

MPRT-DS-IEC822-10