High Performance Single Board Computer

Dual Tualatin/Pentium-III ServerWorks 30LE-T, LCD/CRT SVGA and Dual Ethernet

HiCORE-i6321

General specifications

CPU

Dual Socket 370 FC-PGA/FC-PGA2 supports :

Pentium Tualatin (512 K) up to 1.26 GHz

IntelÆ PentiumÆIII with FSB @ 133/100 MHz

Chipset

ServerWorks ServerSet III LE

BIOS

AWARD Flash BIOS v6.0 Green&Soft Off

function, LS120, Multiple boot function,

FWH 4 MB

Green Function

power saving supported in BIOS. DOZE /

STANDBY / SUSPEND modes, ACPI & APM

Secondary Cache

Integrated on CPU

DRAM Memory

up to 4GB of PC-133 Registered SDRAM in

four 168-pin DIMM sockets

Data Bus & Bus Speeds

64-bit PCI at 66/33 Mhz, 32-bit PCI at 33 Mhz

(onboard device), 16-bit ISA at 8 Mhz

PCI Enhanced IDE with Ultra DMA

supports 2 ports and up to 4 ATAPI devices,

Ultra DMA transfer rates 33 MB/sec

Watchdog Timer

128-level timer generates RESET or NMI when

your application loses control over the system.

Real-time Clock

built-in super I/O with lithium battery backup

for 10 years of data retention. CMOS data

backup of BIOS setup and default.

Flash Disk DiskOnChip® 2000

Package

Single Chip FlashDisk in 32-pin DIP JEDEC

Capacity

up to 288 MByte

PCI bus

Supports 64-bit PCI bus

High Drive ISA64 bus CTI ready

ISA Add-on

64 mA high drive buffer supports up to

20 ISA based add on cards

High Speed Multi I/O

Chipset

SMSC FDC 37B787

Serial ports

2 external high speed RS-232C ports COM1,

COM2 (2x 10-pin box header). Both with

16C550 compatible UART and 16 byte FIFO.

USB

one onboard USB v1.0 port

Floppy Disk Drive Interface

2 floppy disk drives, 5º" (360 KB or 1.2 MB)

and 3½" (720 KB, 1.44 MB).

Bi-directional Parallel Port

SPP, EPP and ECP mode.

Keyboard and Mouse Connectors

external PS/2 KB/Mouse port (2-in1 mini DIN)

onboard AT Keyboard port (5-pin box header)

Network Interface Controller

Chipset

2x Intel 82559, 10/100 Mbps, auto    switching

Connectors

external RJ-45 with LEDs on bracket

Display Controller

Chipset

ATI RAGE XL video

Supports 8 MB SDRAM

System Bus

32-bit PCI bus

Display Type

CRT (VGA, SVGA, XGA, SXGA) & DVI

Compatibility

IBM VGA hardware

System Monitoring and Alarm

Chipset

Winboard W83782D

For CPU & System Temperature, System

Voltage and Cooling Fan RPM

Environmental and Power

Power Requirements

+5 V @ 10.03 A (typical),

+12 V @ 0.44A (typical), -12V @0.08A

(typical);

(FC-PGA2 Tualatin 1.26GHz x 2 at 133 FSB

and 2048 MB PC-133 Registered SDRAM)

Board Dimensions

338 mm x 122 mm.

Board Weight

0.6 Kg.

Operating Temperature

0 to 55°C (32 to 131°F)

Ordering

HiCORE-i6321VL2 : Full-size, Socket 370, FCPGA2

CPU Card for Dual Pentium III/ Tualatin

CPU with Flat Panel/CRT SVGA, Dual Fast

Ethernet and DiskOnChip socket

HiCORE-i6321VL : as above with single Fast

Ethernet port

Dual LAN 10/100

Intel 82559

Dual Socket 370 : Tualatin /

Special features:

Pentium-III, at FSB 100/133. CRT Display .ATI RAGE XL

LCD / DVI . ATI Rage XL

Dual Intel® Tualatin, Pentium® III, , at FSB 100/133

ServerWorks ServerSet III LE

Dual LAN 10BASE-T/100BASE-TX

COM1/COM2 RS-232C, USB

PS/2, KB/Mouse

4 DIMM sockets for up to 4GB registered ECC SDRAM

CRT/ SVGA/ LCD display capability

DiskOnChip® 2000 up to 288 MB

High Drive ISA-bus

Dedicated System Monitor and alert alarm for system management

64-bit PCI Bus run the latest 64-bit high intensive computing applications

DVI Interface for LCD or Gas PLASMA and Hi-RES Flat Panel displays

Cepoint Networks, LLC.sales@cepoint.com  ph 603.883.7979. www.cepoint.com